## Slide 1: Introduction to Weather Radars
Hannah Vagasky
AER Lunch & Learn
August 13, 2024

## Slide 2: Outline
What are radars and how do they work
Brief history of radars
The NEXRAD radar network
Different types of weather radars
  Doppler
  Polarimetric
  Mobile and satellite radars
Weather Radar Analysis
  Bow echo
  Hook echo
  Tornadic winds and debris signatures
How AER uses radar data
The future of radars
Radar resources
https://olympex.atmos.washington.edu/Photos.html

## Slide 3: What are Radars and How They Work?
Radar is an acronym: Radio Detection And Ranging
Definition:
  A system that determines the location of objects by sending out short pulses of radio waves and measuring the time it takes for the wave to be reflected from the objects (Cambridge Dictionary)
  Can be used to detect aircraft, vehicles, ships, missiles, precipitation, birds/insects, and surface variability below ground
https://www.weather.gov/mlb/Doppler_Dual_Pol_Weather_Radar

## Slide 4: How Radars Detect Precipitation
https://www.mdpi.com/2673-4834/3/1/12#B7-earth-03-00012

## Slide 5: Radar Reflectivity
Radar Reflectivity = Amount of power in the radio wave that is returned to the radar
  Proportional to number of detected particles and their cross sectional area
  Reported in dBZ, which is a logarithmic power unit
Weather radars continuously scan the atmosphere making 360º circles at different elevation angles
  The height of the beam increases as it gets further from the radar
Base reflectivity uses data from the scan closest to the surface
Composite reflectivity shows the highest reflectivity in the vertical column
https://www.kfyrtv.com/2022/06/27/morse-code-weather-how-weather-radar-creates-3-d-picture-atmosphere-detect-precipitation/, https://en.wikipedia.org/wiki/Composite_reflectivity,

## Slide 6: Brief History of Radars
German scientists in the late 1800s and early 1900s started to discover that radio waves could be reflected from solid objects and used to detect these objects (ships in fog)
Prior to World War II, numerous countries developed radars for military purposes with great secrecy to track aircraft
The ability for radars to detect precipitation was recognized during World War II.
The development of weather radars in the United States started in 1942 when the US Navy donated 25 surplus radars to the Weather Bureau
  First radar network in the US deployed in 1957
https://www.kfyrtv.com/2022/07/30/morse-code-weather-history-weather-radar-wwii-technology-present-day-applications/
https://en.wikipedia.org/wiki/Radar, https://en.wikipedia.org/wiki/Weather_radar#History

## Slide 7: The NEXRAD Network
NEXRAD = Next Generation Weather Radar
  Current network of 160 weather radars operated by the government
  May also hear them referred to as WSR-88D radars, which is the technical name for the radars themselves (Weather Surveillance Radar 1988)
Timeline
  1970s – The government decided that the previous radar network needed to be upgraded/replaced
  1990 – First operational protype deployed
  1992 – 1997: Nationwide deployment
  2010 – 2013: Radars updated nationwide
Radars are currently Doppler and polarimetric
https://upload.wikimedia.org/wikipedia/commons/e/e4/NEXRAD_map.jpg, https://www.farmforum.net/story/news/2022/06/24/nws-upgrades-sioux-falls-radar-expects-downtime-last-another-week/7722778001/, https://www.heraldandnews.com/news/oregon/noaa-seeks-funding-to-repair-weather-radar-on-mount-ashland/article_1b94efcf-06e5-5cba-8a8d-9164db05dc78.html, https://www.weather.gov/abq/radarslep

## Slide 8: Types of Radars: Doppler
Radars measure the strength and phase of the reflected radio wave
The phase difference between the emitted and returned radio waves is used to determine if the precipitation is moving towards or away from the radar and how fast
  A single radar cannot determine the 3D winds
Longer wavelength
Lower frequency
Smaller wavelength
Higher frequency
The Doppler Effect for a Moving Sound Source
https://www.physicsclassroom.com/class/waves/Lesson-3/The-Doppler-Effect
Idealized Radial Velocity Display
Winds Toward the Radar:
Negative Values
Cool colors
Winds Away from the Radar:
Positive Values
Warm colors
https://www.nssl.noaa.gov/publications/dopplerguide/chapter2.php

## Slide 9: Types of Radar: Polarimetric
At first radars, only emitted and receive horizontally oriented radio waves
Some radars are now able to emit and receive horizontally and vertically oriented radio waves
  Additional radar variables are obtained by comparing the returned power and phase of these different waves
    Example: Differential reflectivity, correlation coefficient
  These additional variables provide insight into the precipitation
    Example: shape, orientation, melting

## Slide 10: Types of Radar: Different Wavelengths
A range of radio wavelengths can be used in weather radars
  The range of wavelengths used is broken into “radar bands”
    The NEXRAD network is S – Band
  Each band has strengths and weaknesses
Sensitive to small drops
Can reliably detect large particles
Obscured by heavy rain
Can penetrate heavy precipitation
Requires smaller antenna and less power
Requires larger antenna and more power
Radar Frequencies and Bands

## Slide 11: Types of Radar: Mobile and Satellite
Diverse group of instruments in terms of mobility/platform and wavelength
Largest
Smallest
Stationary, ”easily” transportable
Ex: NCAR S-Pol (S – Band)
Truck Mounted
Ex: SMART-R and NOXP (X – Band)
Satellite
Ex: NASA GPM Precipitation Radar (Ku- & Ka- Band)
Very active research area
https://global.jaxa.jp/countdown/f23/overview/gpm_e.html, https://www.nssl.noaa.gov/tools/radar/, https://news.ucar.edu/3993/radars-next-phase, https://amt.copernicus.org/articles/13/4521/2020/#&gid=1&pid=1
Aircraft Mounted
Ex: NASA APAR-2 (Ku- & Ka- Band)

## Slide 12: Weather Radar Analysis: Bow Echo
https://www.spc.noaa.gov/misc/AbtDerechos/casepages/apr202011page.htm, https://commons.wikimedia.org/wiki/File:Bow_echo_diagram.svg, https://en.wikipedia.org/wiki/Derecho#:~:text=A%20derecho%20(%2F%CB%88d%C9%9B,as%20a%20mesoscale%20convective%20system.
Bow Echo = Line of storms that arches outward in the direction it is moving
  Often associated with strong straight-line winds, tornadoes are also possible
  May be classified as a derecho if it meets duration and intensity requirements
    Must persist for at least 400 mi, have 58 mph wind gusts along most of its length, and have several, well separated pockets of 78 mph gusts

## Slide 13: Weather Radar Analysis: Super Cells and Hook Echo
Super cell = A storm that contains a deep, rotating updraft
  Least common type of thunderstorm, but most destructive
    Can produce strong tornadoes and large hail
A hook echo is a reflectivity appendage that results from precipitation being wrapped around the back of the rotating updraft
  This is the most likely location for a tornado
https://www.ustornadoes.com/2013/02/14/understanding-basic-tornadic-radar-signatures/, https://www.e-education.psu.edu/meteo3/l9_p9.html
Updraft
Model of a Super Cell
Observed Super Cell on April 27, 2011, in North Carolina

## Slide 14: Weather Radar Analysis: Tornado Signatures
Tornado Vortex Signature / Velocity Couplet
  A tight couplet of strong winds away from and towards the radar
  Often associated with a rotating updrafts (not the actual tornado)
    The radar beam is often too high or the tornado is too small to be directly observed
  A tornado is possible, but not guaranteed
Tornado Debris Signature / Tornado Debris Ball
  One of the polarimetric variables has decreased values when non-meteorological particles are detected (cross correlation coefficient)
  A debris signature occurs when this variable has decreased values in a region with high reflectivity and a velocity couplet
    Indicative of a tornado causing destruction
https://www.noaa.gov/jetstream/velocity, https://www.weather.gov/lmk/nws_radar_dualpol_tordebris

## Slide 15: Weather Radar Analysis: Non-Meteorological
Weather radars detect more than precipitation and have been used to study insect, animal behavior
Blooms
Bugs (and migrating birds) taking off in the evening and flying overnight
Why reflectivity sometimes increases overnight near the radar
Bird Roost Rings
Birds taking off in the morning and flying in all directions
These are purple martins taking off from roosts near lakes in Ohio
Bats
https://www.weather.gov/iln/birds, https://radarscope.zendesk.com/hc/en-us/articles/4416722636946-Biological-Scatter-What-You-Can-See-On-Radar-Other-Than-Rain, https://x.com/NWSSanAntonio/status/447911878635708416

## Slide 16: How AER Uses Radars
Estimation of the height planetary boundary layer
  Planetary boundary layer = lowest layer of the atmosphere and is directly influenced by the surface
  We are using the lowest radar scan and polarimetric variables to determine the top height of this layer and how it changes over time
Derive horizontal and vertical winds
  The velocity from two nearby radars can be used to derive the 3-D winds in a region
    This technique is being used to estimate winds behind a bow echo and in hail producing storms
  We are using the highest radar scan to estimate the horizontal winds directly over the radar behind a bow echo
ICECHIP and Hail Analysis
  Several mobile radars will be deployed during ICECHIP
  Will be used to help us understand the evolution of the hail and determine the winds within the storm
https://www.tceq.texas.gov/downloads/air-quality/research/reports/misc/5822345974015-20240626-planetary-boundary-layer-pbl-verification-with-2022-tracer-aq-field-study-data.pdf, https://earthsky.org/earth/nws-upgrades-to-dual-polarization-radar-for-better-look-at-precipitation-tornadoes/

## Slide 17: The Future of Radars
The Future of the NEXRAD Network
  Part of Weather Act Reauthorization Act of 2023 requires that the NEXRAD network be replaced by 2040
    Currently in the planning and development phase
    The next generation of radars will be Phased Array Radars.
      These radars have flat panels that are stationary, which will allow for more flexibility in how the radar scans
      The National Weather Service’s phased array radar was a decommissioned radar from the US Navy in 2003
Commercialization of radar data
  “Gap Filling” Radars
    Large portions of the country have poor NEXRAD radar coverage
    Private companies such as Climavision have started to try to tackle this issue
      24 X-band radars deployed at the end of 2023, plans for a total of 200
  Satellites
    Many portions of the world, especially in poor nations, lack radar coverage
    Companies such as Tomorrow.io are launching a suite of Ka-Band radars to provide global coverage that is updated more frequently
      Several launched since 2023, data available as of 2024
https://www.tomorrow.io/blog/tomorrow-io-announces-successful-precipitation-scans-from-its-space-radars/, https://www.bizjournals.com/louisville/inno/stories/news/2024/01/24/climavision-radar-install-weather-tech-dry-ridge.html, https://www.congress.gov/bill/118th-congress/house-bill/6093/text/ih#toc-HA36573D5DAC24FFA91DFFFE25CF1771A

## Slide 18: Radar Resources
RadarScope
  My favorite app, available in all app stores
NWS Radar Website
  https://radar.weather.gov/
Alternative Radar Website
  Less user friendly
  https://weather.cod.edu/satrad/?parms=continental-conus-comp_radar-24-0-100-1&checked=map&colorbar=undefined